ALMA – GMVA obs. Mode I
- ALMA: 32x 62.5 MHz in X/Y pol
  - Usable: 51.2 MHz due to overlapping sub-bands
  - 16 Gbps Mark 6 recording
- VLBA: 2x 128 MHz in R/L pol
  - |------------|------------| 2x 128 MHz VLBA
  - |-----|-----|-----|-----| 4x 62.5 MHz ALMA
  - 2 Gbps Mark 5C
- DBBC2: 512 MHz in R/L pol (no sub-bands)
  - Has to overlap with VLBA band
  - 4 Gbps Mark 6, Flexbuff, Mark 5C (single pol. 5B+)

---
ALMA – GMVA obs. Mode II
- VLBA freqs:
  - sample_rate = 256.000 Ms/sec; * (2bits/sample)
  - chan_def = : 86140.00 MHz : U : 128.00 MHz : &CH01 : &BBC01 : &NoCal; *Rcp
  - chan_def = : 86140.00 MHz : U : 128.00 MHz : &CH02 : &BBC02 : &NoCal; *Lcp
  - chan_def = : 86268.00 MHz : U : 128.00 MHz : &CH03 : &BBC03 : &NoCal; *Rcp
  - chan_def = : 86268.00 MHz : U : 128.00 MHz : &CH04 : &BBC04 : &NoCal; *Lcp
- Band starts at lower edge of normal GMVA mode!
  - sample_rate = 1024 Ms/sec; * (2bits/sample) * 512 MHz BW!!
  - chan_def = : 86524.00 MHz : L : 512.00 MHz : &CH01 : &BBC01 : &U_Cal; *Rcp
  - chan_def = : 86524.00 MHz : L : 512.00 MHz : &CH02 : &BBC02 : &U_Cal; *Lcp
    - Corresponds to 86012.00 MHz @lower edge

---
ALMA – GMVA correlation
- LSB will be converted automatically to USB
- Use “zoom” mode in correlation to split VLBA/EVN bands
- Due to different sampling rates → funny freqs.
  - 86330.290625 MHz bw 51.2 MHz
  - 86271.696875 MHz bw 51.2 MHz
  - 86213.103125 MHz bw 51.2 MHz
  - 86154.509375 MHz bw 51.2 MHz
    - All lower edges!

---
ALMA – GMVA obs. test
- Test done with VLBA, ALMA, Effelsberg
- Fringes found:
  - VLBA – ALMA
  - VLBA – Effelsberg (RDBE)
    - Bug in DBBC2 512 MHz DSC mode
- Conversion of XX, YY, XY, YX, RY, LY, RX, LX...
  - polconvert after correlation (OSO, Marti-Vidal)
- Further analysis at Haystack (Mathews)

---
GMVA tests – ALMA mode
- At present: debugging of 512 MHz DSC mode
  - Local at Effelsberg: RDBE, DBBC2 (Mark 5B+), DBBC2 (FiLA10G → Mark 6/Flexbuff)
  - Additional problem with Mark 6, JIVE5abc6 and 4 Gbps: lost packets
    - Additional test with Haystack Mark 6 software planned
- GMVA-wide test at the end of next 2 sessions
  - May session: 4 hours with:
    - VLBA, GBT, On, Mh, Eb, Ys

---
GMVA tests
- New PFB firmware will be used (incl. DSC mode)
- Setup for FiLA10G different:
  - 2 VDIF threads (L&R) via 2 streams
    - Can be combined standalone or by correlator software
- Recipe and firmware will be distributed asap